## Slide 1
UE20CS253: Computer Networks
Vishwa Mehul Mehta
Software Defined Network (SDN)
PES2UG20CS389
NAME:
SRN:
SEC:
4-F
1

## Slide 2
Introduction
Software-defined networking (SDN) is an architecture that abstracts different, distinguishable layers of a network to make networks agile and flexible.
2
In a software-defined network, a network engineer or administrator can shape traffic from a centralized control console without having to touch individual switches in the network. A centralized SDN controller directs the switches to deliver network services wherever they're needed, regardless of the specific connections between a server and devices.

## Slide 3
Purpose of the Protocol
The goal of SDN is to improve network control by enabling enterprises and service providers to respond quickly to changing business requirements.
It provides separation between the control plane (controller) and data plane (switch) functions of networks using a protocol that modifies forwarding tables in network switches.
3

## Slide 4
Message format/Architecture details
A typical representation of SDN architecture comprises three layers: the application layer, the control layer and the infrastructure layer. These layers communicate using northbound and southbound application programming interfaces.
OpenFlow is an open standard for a communications protocol that enables the control plane to break off and interact with the forwarding plane of multiple devices from some central point, decoupling roles for higher functionality and programmability.
4

## Slide 5
Message format/Architecture details
All OpenFlow message instances are subclasses of the OpenflowMessage abstract class. Every message includes an internal header instance that encapsulates:
  The protocol version
  The message type
  The message length (in bytes)
  The transaction ID (XID)
5

## Slide 6
Message format/Architecture details
6
In addition to the header, specific messages might include:
  Data values, such as port number, number of bytes processed, metadata mask, and hardware address.
  These values are represented by Java primitives, enumeration constants, or data types.
  Other common structures, such as Ports, Matches, Instructions, Actions, etc.
  These structure instances are all subclasses of the OpenflowStructure abstract class.

## Slide 7
Usage
  Software-defined environment (SDE) integration
  Network management and provisioning
  Microsegmentation and zero-trust policies
  Network service chaining
  DevOps
  Campus networks
  Service provider networks
  Data center security
7

## Slide 8
Conclusion
Software-defined networking has had a major effect on the management of IT infrastructure and network design. As SDN technology matures, it not only changes network infrastructure design but also how IT views its role.
8
SDN architectures can make network control programmable, often using open protocols, such as OpenFlow. Because of this, enterprises can apply aware software control at the edges of their networks. This enables access to network switches and routers, rather than using the closed and proprietary firmware generally used to configure, manage, secure and optimize network resources.

## Slide 9
Conclusion
While SDN deployments are found in every industry, the effect of the technology is strongest in technology-related fields and financial services.
9
SDN is influencing the way telecommunications companies operate. For example, Verizon uses SDN to combine all its existing service edge routers for Ethernet and IP-based services into one platform. The goal is to simplify the edge architecture, enabling Verizon to enhance operational efficiency and flexibility to support new functions and services.

## Slide 10
Thank you!!
1st May, 2022
10